## Slide 1: 2D Mesh NoC Implementation
鍾宇騫
2022 / 05 / 23

## Slide 2: Progress
Router implementation by Vitis HLS
  Router architecture
  FIFO buffer (Virtual channel)
  Input unit
  Output unit
  Arbiter
  Switch
  Performance
4 Routers System
  Architecture
  Problems

## Slide 3: 5x5 Router Architecture (router_top.h)
...
Virtual Channel 4
Input Unit 4
…
Virtual Channel 0
...
Virtual Channel 4
Input Unit 0
Virtual Channel 0
…
Output Unit 0
FIFO Buffer
Output Unit 4
FIFO Buffer
Arbiter
Input Flit 0
Input Valid 0
VC Full 0
Input Flit 4
Input Valid 4
VC Full 4
Output Flit 4
Output Valid 4
VC Full 4
Output Flit 0
Output Valid 0
VC Full 0
…
…
…
…
Reference: https://www.sciencedirect.com/topics/computer-science/output-virtual-channel
Control
Data out
Data in

## Slide 4: FIFO Buffer (flit_buffer.h)
Buffer for input unit and output unit
64x104b BRAM
B0
B1
B2
B61
B62
B63
…
Read index = 2
…
read data
…
Write data
enable[64]
Write
Write index = 1
write data & enable
Read

## Slide 5: Input Unit (input_unit.h)
Virtual Channel 0
Input Flit 4
Input Valid 4
VC Full 4
Virtual Channel 1
Virtual Channel 2
Virtual Channel 3
Virtual Channel 4
Flit to switch
Flit valid
Requests[5]
Grants[5]
MUX
Routing

## Slide 6: Output Unit (output_unit.h)
Switch Flit
Switch Valid
FIFO Full
FIFO Buffer
Output Flit
Output Valid
VC Full

## Slide 7: Arbiter (arbiter.h)
Round-Robin Arbitration
  Each output port pass priority to next input unit after sending 5 flits
    If send 0~4 flits and request valid, keep the priority
    If send 5 flits, pass the priority
    If send 0 flits and no request, pass the priority
    If send 1~4 flits but no request, keep the priority
Arbiter
Requests[5][5]
Grants[5][5]
Output FIFO State[5]

## Slide 8: Mux Based Switch (router_top.h)
MUX
VC0
VC1
VC2
VC3
VC4
VC0
VC1
VC2
VC3
VC4
MUX
MUX
MUX
MUX
FIFO
FIFO
Input Unit 0
Input Unit 4
Output Unit 0
Output Unit 1
FIFO
Output Unit 2
FIFO
Output Unit 3
FIFO
Output Unit 4
…
…
…
…
…
…
Switch

## Slide 9: Performance
Spec
  Flit size: 104 bits
  5 input ports (104*5 = 520 bits)
  5 output ports (104*5 = 520 bits)
Clock frequency: 100 MHZ (clock period 10ns)
Random testcases
  Input: each input ports 2,000 random destination flits
  Output: always not full => no blocking situation
  Latency: 2188 cycles
  Throughput: 2,000 flits*5 ports*104bits/(2188 cycles*10ns) = 5.94 GBps
  Ideal throughput: 104 bits * 5 ports* 100MH = 6.5 GBps
  Worst throughput: 104 bits * 1 port* 100MHZ = 1.3GBps

## Slide 10: 4 Router System (system_top.h)
Use testbench simulate NI
  Fetch flits from main memory
  Send flits to router
  Receive flits from router
Router
Router
Router
Router
Input
memory
Output
memory
Input
memory
Output
memory
Input
memory
Output
memory
Input
memory
Output
memory
Design

## Slide 11: Problems
Co-simulation will stuck if let II = 1, but work when II = 3
Synthesis result is not what I want: comb part has registers, but sequential part has only wire
While(1) {
#pragma HLS PIPELINE II=1
Load flits from memory to input wire
Store flits from output wire to memory
Update 4 routers combinational parts (next_state)
Update 4 routers sequential parts (state = next_state)
}